## Slide 1: Reconsideration Requests

## Slide 2: 40 CFR § 112.20(i)(2) - Formal Request for FRP Reconsideration (Not for SPCC)
“In the event the owner or operator of a facility believes a change in the facility's classification status is warranted because of an unplanned event or change in the facility's characteristics (i.e., substantial harm or significant and substantial harm), the owner or operator may submit a request for reconsideration to the Regional Administrator and provide additional information and data in writing to support the request. The Regional Administrator shall consider the request and render a decision as rapidly as practicable.”

## Slide 3: FRP Reconsideration Request Reasons
Facility Reduces Aggregate Oil Storage Capacity to less than 1,000,000 Gallons (e.g., tank re-rating)
Modified Facility Configuration (piping, tanks removed or permanently closed, loading racks, etc.)
Substantial Harm Criteria Change (Spill history expires, water intake removed, etc.)
WOTUS
Notes: Facility Reduce Oil Storage Capacity to less than 1,000,000 Gallons:
Modified Facility Configuration: Piping/Breakout tanks/Removing or permanently closing tanks/Loading Tracks
Documentary evidence that all truck and loading activities have ceased
Photos of blind flanges and/or air gaps installed in the piping between the truck unloading area and the storage tank with contextual photos of the truck unloading area and the tank around the blind flange or air gap to show that the truck unloading area is out of service and isolated from the active storage tank.
Documentary evidence and photographic evidence that the truck unloading tanks were emptied, taken out of service, and clearly marked “Out-of-Service.

## Slide 4: How to Submit FRP Reconsideration Requests in Region 8
Send signed letter R8_FRP@epa.gov
Provide supporting documentation or work with us to schedule an inspection to verify
Request for Information or a Decision (~45 days)
Maintain FRP until decision is made

## Slide 5: Examples – Facility Modifications
The Station no longer has any truck loading racks and associated tanks. The tanks located at the Station are “breakout tanks” and exclusively “transportation related” by definition from 40 CFR 112, appendix A section ii, and as such, meet the exemption from EPA FRP jurisdiction, as outlined in the MOU between the Secretary of Transportation and Administrator of the EPA.
Facility is requesting a formal reconsideration of the FRP status as the overall storage capacity has decreased from 31 storage tanks with a capacity of 1,432,200 gallons to 21 storage tanks with a capacity of 970,200 gallons. Six (6)‐1,100 bbl tanks have been removed from the facility and are utilized at a well production pad. Four (4)‐1,100 bbl tanks are permanently out of service and remain onsite. A total of 10 storage tanks were removed from the facility or permanently removed from service. The following notates which tanks were removed from location and which are permanently out of service. The permanently out of service tanks are blind flanged and labeled at permanently out of service.
Attachment A includes photos/videos of the disconnected tanks.

## Slide 6: Often Need Videos/Photos, Engineering Analysis and Surveys, or On-Site Inspection
WOTUS Jurisdiction Changes
Flow Pathway Changes
Engineering Controls
Out-of-Service Tanks/Truck Racks
Include ample supporting evidence to expedite complete review and approval

## Slide 7: Example Reconsideration Requests
Letter signed by facility management
Explain what’s changing and cite rationale by regulation
Provide supporting documentation

## Slide 8: Supporting Documentation