## Slide 1: Oil Spill Response Deep Dive and Case Studies
Kyle Corcoran

## Slide 2: Module Objectives
To have a better understanding of the roles of the Primary QI (Incident Commander) and Alternate QI (Operations Lead) during the initial response stage, containment and recovery stage, and removal and remediation stages of a response.

## Slide 3: QI Duties and Responsibilities
Notifications
Recall Response Team
Assess Human Health Risks
Spill Size-Up
Activate Alarms
Cleanup
Spend Resources
Protect Wildlife & Cultural Resources
Firefighting and Rescue
Waste Disposal
40 CFR Part 112.20(h)(3)(ix)
Notes: Incident Command System
Spill Response Equipment
Location of ERAP/FRP
OSROs

## Slide 4: Oil Spill Response Phases
Early – Initiating Notifications and Quick Response Actions/Source Control
Intermediate – Spill Containment/Recovery
Transition – Organizing, Removal Actions
Recovery – Unified Command, Cleanup, Restoration

## Slide 5: Oil Spill Response Phases
Early – Initiating Notifications and Quick Response Actions/Source Control
Intermediate – Spill Containment/Recovery
Transition – Organizing, Removal Actions
Recovery – Unified Command, Cleanup, Restoration

## Slide 6: Notifications, Initial Response Actions, and Source Control
Primary vs Alternate QI responsibilities

## Slide 7: Apple Valley Spill – Fog of the Initial Response
Report of gasoline spill in North St. Vrain River
  No, it’s a diesel spill.
  No, it’s both gasoline and diesel.
  No, nothing is in the river.
Mobilized EPA contractors with specific directions.
  Bring spill trailer, vac truck, manpower, etc
  Bring air monitoring and water sampling equipment.
Notes: Messages:
An initial spill response can be a bit like the telephone game we played as kids. You need to be as clear and specific as possible to minimize mistakes.
The Colorado State Patrol filed the spill report with the NRC. We received a direct phone call that said gasoline, but the NRC spill report said diesel. We responded to gasoline and fortunately were correct.
It was gasoline and it was in the river. It closed the main highway and access to Estes Park and Rocky Mountain National Park. There were thousands of dead fish in the River. I didn’t hear about the dead fish for hours. They had all floated and washed up downstream in public parks and in people’s backyards.
As we coordinated the response, we were very specific about what equipment we needed. We didn’t say, “Hey, there’s a gasoline spill in the St. Vrain. We need you to respond.” We said “We have a report of gasoline in the river from a tanker truck. We need you to bring…. “
We talked through the situation with our contractors to ensure we were as prepared as possible. Even with that preparation, we didn’t have everything. I wanted to sample for benzene emissons from the gasoline. That is a specific type of equipment that the crew hadn’t thought to grab as they deployed.
You’ll hear us repeat over and over again: Oil spill responses are all-hands on deck. We had sub-contractors who decided they didn’t want to work late so they walked off the job. I and another OSC colleague literally jumped into mix and pour to concrete. Ken Dockweiler and I would adjust boom during Ash Coulee.
Key TakeAway:
Transition: This is also why the source control and size up is important. You want to ensure you have the right resources. Miscellaneous Info:

## Slide 8: Open Discussion for Primary QI or Incident Commander: Notifications
Where is your emergency phone list located?
How would your facility stand up an Incident Management Team? Is the QI the IC? Corporate IC?
How would your facility discover a spill? For unmanned facilities, how do you make sure that a spill is discovered quickly?

## Slide 9: Open Discussion for Primary QI or Incident Commander: Notifications
Where is your emergency phone list located?
How would your facility stand up an Incident Management Team? Is the QI the IC? Corporate IC?
How would your facility discover a spill? For unmanned facilities, how do you make sure that a spill is discovered quickly?

## Slide 10: Incident Command
Primary QI is the initial Incident Commander
Take command and delegate:
  “Make notifications. Call the NRC.”
  “Secure the scene. Is it safe to respond?
  “Close the valves. Grab the spill trailer and deploy boom.”
  Set up staging areas for waste management/disposal
Initial Day 1-2 objectives for the Ash Coulee Spill Response
Primary QI or Incident Commander
Notes: Messages:
In the beginning, these were our objectives on Day 1 and 2 of the Ash Coulee spill response…
Safety
Controlling the spill with recovery
Assessing impacts to wildlife, in particular cattle.
As QI, your special power is your ability to communicate and coordinate.
When you are in training, practice this approach. When we visit for an inspection and a GIUE, practice this approach.
Key TakeAway:
Transition: Miscellaneous Info:
Photo dated 12/7/2016

## Slide 11: Notify and provide necessary information to the appropriate Federal, State, and local authorities.
Why is it important to notify these agencies?
  It's required by law, and some of the agencies will join Unified Command in the response.
  Be as accurate as possible with the spill quantity and potential impacts. You want responders to be prepared for the response.
  Early notification and communication builds trust with community and regulatory agencies.
Primary QI or Incident Commander
Notes: Messages:
Your NRC notification ensures all these other agencies are notified. We have resources that we bring to the spill response.
Key TakeAway:
Transition: Miscellaneous Info:
Share Trans Canada Pipeline spill in SD vs. recent ammonium nitrate response with 4 responders.

## Slide 12: Common Notification Issues
Staff can’t find the FRP or list of notifications
National Response Center (NRC) should be one of the first calls
Response contractors are not available
Lack of clarity over who calls who
Balancing notifications with implementation of response plan
Notes: In almost every scenario, your notification list may be out of date. It’s really hard to maintain current phone lists.
Take notifications seriously. Recommend delegating notifications and implementation of response plan. These need to occur simultaneously within the first hour

## Slide 13: Assessments and Source Control
Safety is the priority!
Secure the Release. A key priority
Source control includes shutting in pipeline; plugging tank; building berms to contain the spill; etc.
Assessment of the spill includes type of oil, quantity, flow path, safety, etc.
Excavated pipeline during Ash Coulee Spill Response
Alternate QI or Operations Lead
Notes: Messages: Make it stop! Stop the hemorrhage. You don’t need to excavate a pipeline to shut it in. If you have a pipeline break, your control room would likely shut in the line.
You’ve activated the internal alarms. You’ve notified and mustered your team. You’ll have a brief, ensure safety and then secure the release and begin sizing up the spill.
Do what you can to slow or stop the spill safely.
Assessing the spill what type of oil is it? How does it behave? What are safety risks? This informs how you will respond.
Key TakeAway:
Transition: Miscellaneous Info:

## Slide 14: Field Reconnaissance and Assessments
Assessment and initial response during Ash Coulee Spill
Alternate QI or Operations Lead
Notes: Messages:
These are photos from Ash Coulee Spill. It was 12,000 – 14,000 bbls of Bakken crude oil in a small creek in ND. Your first estimate will be a wild guess. Operator didn’t report a 12,000 bbl spill. It took time and analysis to develop that access. But they also didn’t say “hey, we’ve had a small spill in a creek.”
I still remember the sinking feeling I had when I first arrived at Ash Coulee and saw the extent of the spill. The enormity and the implications were hard to grasp initially. To quote Operator “Holy Buckets!”
Report of oil from the rancher. The team responds and installs boom in the creek before a winter blizzard. They safely retreat. Notifications made.
It's extremely difficult to size up spills and estimates with environmental conditions and can always do a follow up report with the NRC.
Key TakeAway:
Transition: Miscellaneous Info:

## Slide 15: Source Control
Includes pre-installed and engineered structures to contain the release.
CSP plugging and removing gasoline tanker
Pre-installed gates culverts for source control.
Alternate QI or Operations Lead
Notes: Messages: Securing the release is one of the top priorities during a spill response. These are some more examples of what the source control may look like.
This the Colorado Hazmat during the same Apple Valley ER gasoline spill. They plugged the tanker, off-loaded it and then removed the damaged tank.
Anadarko Petroleum installed gates on their culverts so they could quickly contain a release from their facility. This is an engineered source control near their facility.
Key TakeAway:
Transition: Miscellaneous Info:

## Slide 16: Open Discussion for alternate QI or Operations Lead: Source Control and Assessments
What are the number 1 and 2 priorities of a spill? And what does that entail on your facility?
What information is needed for a proper notification?
Why is it important to call the NRC and EPA? What information needs to be provided? Does the info given need to be perfect?

## Slide 17: Open Discussion for alternate QI or Operations Lead: Source Control and Assessments
What are the number 1 and 2 priorities of a spill? And what does that entail on your facility?
What information is needed for a proper notification?
Why is it important to call the NRC and EPA? What information needs to be provided? Does the info given need to be perfect?

## Slide 18: Summary: Initial Steps for the QIs during Response
Sound the alarms
Notify response team
Stop the source.
Conduct initial assessment
Notify external agencies. Call the NRC.
Plains Pipeline Initial Assessment on Little Beaver Creek 2017
Notes: Messages: Remember. Think like your first aid training. You are the incident commander directing the action for your team.
Ensure internal alarms,
Notify and muster your response team.
Brief on the situation and direct the response.
“Grab the response trailer. Assess the scene. Secure the spill, if you can do so safely.”
Make those external notifications.

## Slide 19: Containment and Recovery Actions
Primary vs Alternate QI responsibilities

## Slide 20: Case Study: Red Butte Creek Pipeline Spill
June 11-12, 2010
Salt Lake City, UT
800bbls/33,600 gallons from 10” crude pipeline
Red Butte Creek/Jordan River
Knowing Discharge Pathways
Notes: FD chased vapor concerns
Lightning strike on fence arc welded into pipeline.
People were complaining about vapor
Imagine a spill that happens for a matter of ours in a downtown area. Downtown SLC – main city park.

## Slide 21: Open Discussion for Primary and Alternate QIs: Prompt Removal Actions
What do you have in your spill trailers, and is that adequate for a small spill? A worst-case discharge?
What are the primary goals when containing the spill and initiating prompt removal actions?
Notes: Answer: Source control. Follow up Q: why is Source control the primary goal? A: because if you stop the spill, its no longer growing. If you have resources available, stop the source, and get ahead of the leading edge of the spill. Maybe the source control is putting in culvert plugs so the spill does not continue to leave your property, maybe its closing a valve, regardless of what it is, have a plan of attack and stick to it.
Answer: hopefully. We know a lot of these plans are written by contractors that likely have never visited the site. You as primary responders to a spill have the knowledge of the facility to know where a spill will go, and how it will get there. Its OK if the plan is different now, but when you notice a change is needed, please make that change. Remember the GIUE is based on what is in the plan.
Answer: small spill, yes. WCD, maybe.

## Slide 22: Open Discussion for Primary and Alternate QIs: Prompt Removal Actions
What do you have in your spill trailers, and is that adequate for a small spill? A worst-case discharge?
What are the primary goals when containing the spill and initiating prompt removal actions?
Notes: Answer: Source control. Follow up Q: why is Source control the primary goal? A: because if you stop the spill, its no longer growing. If you have resources available, stop the source, and get ahead of the leading edge of the spill. Maybe the source control is putting in culvert plugs so the spill does not continue to leave your property, maybe its closing a valve, regardless of what it is, have a plan of attack and stick to it.
Answer: hopefully. We know a lot of these plans are written by contractors that likely have never visited the site. You as primary responders to a spill have the knowledge of the facility to know where a spill will go, and how it will get there. Its OK if the plan is different now, but when you notice a change is needed, please make that change. Remember the GIUE is based on what is in the plan.
Answer: small spill, yes. WCD, maybe.

## Slide 23: Coordinate rescue and response actions as previously arranged with all response personnel
What is in your ERAP/FRP?
  Is it easy to find in an emergency?
  Is it scalable?
OSRO and response team responsibilities
  What role do they play in the FRP?
Other options
  Co-ops, state and local resources, EPA and the Regional Response Team
Primary QI or Incident Commander

## Slide 24: Scalability
When do you know you need help?
When do you call in a national
OSRO?
How long does it take to get
them on site?
Who is available locally to
respond? Have you already
called them for the initial spill
Response?
Primary QI or Incident Commander
Notes: Summit Mid-stream: Black tail creek spill. Everything was under control until the snow melted and broke through every damn we had in place.
Discuss

## Slide 25: Use authority to immediately access company funding to initiate cleanup activities;
What items/resources do you think will typically need to be procured during a response?
  Contractor resources, absorbent boom, porta-johns, etc.
When is too much equipment/materials.
  Watch out for over-billing and think about resources needed vs have.
Primary QI or Incident Commander

## Slide 26: Containment Boom Deployment
Alternate QI or Operations Lead
Notes: Can have less than 1,000 feet of boom if drainage is small

## Slide 27
Alternate QI or Operations Lead

## Slide 28
Alternate QI or Operations Lead

## Slide 29
Alternate QI or Operations Lead

## Slide 30: Containment Boom Alternatives
“As appropriate” in FRP rule provides inland plan holders flexibility – added to PREP Guidelines in 2016
Alternative strategy may be more appropriate where spill pathway could be a dry drainage pathway or tributary
Alternatives include: underflow dams, temporary containment, dams (soil, etc.), inflatable diaphragms (culvert plugs)
Alternate QI or Operations Lead
Notes: Authority for variations comes from 40 CFR part. 112, Appendix E, Section 3.3
“The response resources shall, as appropriate, include:”

## Slide 31: Photos of DDD
Alternate QI or Operations Lead

## Slide 33: Is the Oil the brown stuff?
Contractor oversight is critical!
If the contractor fails to perform, it reflects on the responsible party.
Oil spill responses require more hands-on engagement than a normal construction job
Alternate QI or Operations Lead
Notes: This was the response from the OSRO when asked why they weren't recovering oil contained within the boom? They were just watching the oil build up behind the boom until it went under the boom and further down the canal. While there are no dumb questions... this tells you why you need oversite over your contractors on a response.
Spill response is a crappy job. Its demanding physical labor, hard hours in the field away from home. There are a lot of new people that enter the field working for contractors. You need to make sure they have the knowledge and awareness to do the job and do it safely.

## Slide 34: Open Discussion: Containment and Recovery Actions
How do you scale up a response? Have you ever trained on how that works logistically?
In a worst-case spill, how would you provide oversight to contractors?
What role does an OSRO, Co-op, local agencies, etc. play in your spill plans?

## Slide 35: Open Discussion: Containment and Recovery Actions
How do you scale up a response? Have you ever trained on how that works logistically?
In a worst-case spill, how would you provide oversight to contractors?
What role does an OSRO, Co-op, local agencies, etc. play in your spill plans?

## Slide 36: Removal and Remediation Actions

## Slide 37: Case Study: Silvertip Pipeline Spill
July 1-2, 2011
Laurel, MT
1,000 bbls/42,000 gallons from 12” Bighorn crude pipeline
Yellowstone River
Flooding and Oil Spill Impacts
Public/Media/Congress Interest
Unified Command Challenges
https://response.epa.gov/ExxonMobilPipelineSpillYellowstoneRiver

## Slide 38: Oil Spill Response Waste Management
Waste Streams
Oil
Oily Water
Sorbents
Soil/Topsoil
Oiled Vegetation/Debris
PPE
Crops/Fodder
Disposal/Treatment Methods
In-Situ Burns
Subtitle D Landfills
Hazardous Waste Landfills
Landfarming/Composting
Incineration/Air Curtain Burner
Recycling
Natural Attenuation
FRP Appendix F Disposal Plans 1.7.2.1

## Slide 39: AirCurtain Burners
Notes: Figure out why video isn’t working.

## Slide 40: Silvertip Pipeline Response – Hayfield Staging Area
Responsible party identified available land near the spill source site
Mowed and collected the hay and leased the land for use as staging
“Quiet” side of the river, away from Billings and easily secured

## Slide 41: Transferring Incident Management
Integrating State and EPA in a command post
Coordination on messaging and incident objectives
Contract support for incident management, planning section, or claims
Sustainability and rotations without losing continuity

## Slide 42: Direct cleanup activities until properly relieved of this responsibility
EPA Typically NOFI - Notice of Federal Interest – EPA is interested in what is going on and will be part of UC.
Clean Water Act - 311 order
NOFA - Notice of Federal Assumption – EPA is taking over the response. Its better and much cheaper for you to spend your money vs me spending your money for you.
Primary QI or Incident Commander
Notes: A lot of questions about the transition to UC.
If an additional IC is coming on site, the transition should include all pertinent information including past actions and plans moving forward.

## Slide 43: Open Discussion: Removal and Remediation Actions
How do you get rid of waste? Oily water, debris, PPE, etc.
How does your company handle large spills and the transition from you to a national Incident Management Team?
Do you have a pre-determined staging area? Do you have access to that area?

## Slide 44: Open Discussion: Removal and Remediation Actions
How do you get rid of waste? Oily water, debris, PPE, etc.
How does your company handle large spills and the transition from you to a national Incident Management Team?
Do you have a pre-determined staging area? Do you have access to that area?